Simulation of Beam Hardening Effect in CT
Maciej Zajkowski

---
Radon Transform

---
Radon Transform

---
Sinogram
- Any object can be described as sum of points with different coordinates
- Radon transform of any object consists out of many sinusoids

---
Types of CT

---
Reconstruction
FBP - The most commonly used analytical reconstruction methods on commercial CT scanners are all in the form of filtered backprojection, which uses a 1D filter on the projection data before backprojecting the data onto the image space. The popularity of FBP-type of method is mainly because of its computational efficiency
Iterative reconstruction, reconstructs images by optimizing an objective function, which typically consists of a data fidelity term and an edge-preserving regularization term. The optimization process in IR involves iterations of forward projection and backprojection between image space and projection space. Lower image noise and higher spatial resolution
https://www.imagewisely.org/Imaging-Modalities/Computed-Tomography/Image-Reconstruction-Techniques

---
Vamvakeros, Antonis. (2017). Operando chemical tomography of packed bed and membrane reactors for methane processing.

---
Beam Hardening
- Beam hardening is the phenomenon that occurs when an x-ray beam comprised of polychromatic energies passes through an object, resulting in selective attenuation of lower energy photons.
  - Mean energy increases because lower energy photons are absorbed more rapidly than higher- energy photons
- The effect is conceptually similar to a high-pass filter in that only higher energy photons are left to contribute to the beam, and thus, the mean beam energy is increased ("hardened")

---
Beam hardening – artefacts
CT beam hardening artifacts have two distinct manifestations:
- streaking
- cupping artifacts.
[1 ]Cao, W. (2019). Development of Beam Hardening Correction Algorithms for Industrial Computed Tomography.

---
Simulation of polichromatic attenuation
- Wn – unknown vector of N photon energy weights
- μn – vector of N linear attenuation coefficient
- Tm – vector of M material thickness.
- Im/I0 – vector of M X- ray transmission measurements
[2] Lifton, J. J., Malcolm, A. A., & McBride, J. W. (2014). A simulation-based study on the influence of beam hardening in X-ray computed tomography for dimensional metrology. Electro-Mechanical Engineering Group, The University of Southampton, UK; Singapore Institute of Manufacturing Technology, Precision Measurements Group, Singapore.

---
[2]

---
- “X-ray transmission is measured using two step wedges, one aluminium and one titanium.
- The transmission measurements are made at a single source voltage of 160 keV and a target current of 10 μA. The thicknesses of the stepwedges vary from 1 mm to 26 mm in steps of 1 mm ± 0.1 mm. During the transmission measurements the X-ray source is collimated to minimise the scatter signal. [...]
- Each term in the coefficient matrix of Eq is pre-calculated with knowledge of the material thickness t and values of μ from NIST “
[2]

---
Data

---
Data - view

---
Sinograms

---
Reconstructions

---
SI metric
- Ip1,Ip2 – peaks
- Iv1,Iv2, -valleys
- C – maximum gray value
- Mb – average gray value of the background
[1]

---
CI metric
[1]

---
[1]

---
Correction algorithms
- Single-material linearization
- Multi-material linearization
- Dual energy
- Iterative reconstruction
[1]

---
[1]

---
Bibliography
- [1 ]Cao, W. (2019). Development of Beam Hardening Correction Algorithms for Industrial Computed Tomography.
- [2] Lifton, J. J., Malcolm, A. A., & McBride, J. W. (2014). A simulation-based study on the influence of beam hardening in X-ray computed tomography for dimensional metrology. Electro-Mechanical Engineering Group, The University of Southampton, UK; Singapore Institute of Manufacturing Technology, Precision Measurements Group, Singapore.
- NIST XCOM: Photon cross sections database, http://www.nist.gov/pml/data/xcom.
- https://www.imagewisely.org/Imaging-Modalities/Computed-Tomography/Image-Reconstruction-Techniques
- Stierstorfer K, Rauscher A, Boese J, Bruder H, Schaller S, Flohr T. Weighted FBP--a simple approximate 3D FBP algorithm for multislice spiral CT with good dose usage for arbitrary pitch. Phys Med Biol. 2004 Jun 7;49(11):2209-18. doi: 10.1088/0031-9155/49/11/007. PMID: 15248573.
- Wykład “Transformacja Radona I Hougha” – dr inż. Robert Kazała

---
Thank you!